## Slide 1
Condition Monitoring of Electrical Machines Using IoT
Created By Agya Aboagye-Otchere & Edem Bleboo
Electrical Engineering Capstone
Supervised By Dr. Stephen K. Armah and Dr. Robert Sowah

## Slide 2
Outline
1
1. Introduction and Background
Introduction and Background
2
2. Design choices
Sensor choice and placement, Flow Diagram
3
3. Design methodology
Design methodology
4
4. Data Communication And Storage
Data Communication And Storage
5
5. Data Collection, Analysis and Results
Data Collection, Analysis and Results
6
6. Conclusion
Achievements and Future Works

## Slide 3
Introduction
Electrical machines:
Induction motors account for 85 % of all Industrial motors
Induction motors faults:
Mechanical: Bearing faults, Shaft Misalignments,
Broken Rotor bar.
Electrical faults: Stator winding faults, Insulation failure.
Existing solutions:
Scheduled maintenance
Reactive maintenance
Condition based maintenance:
Real time
Key parameters

## Slide 4
By using a network of sensors to monitor relevant motor attributes the state of a motor can be evaluated, and early maintenance can be performed to extend motor life.
PROPOSED SOLUTION
Condition Monitoring

## Slide 5
Design choices
Sensor choice and placement:
MPU6050 Accelerometer
PZEM-004T sensor
Digital Hall effect sensor
GY906 infrared thermometer

## Slide 6
Design Methodology
1
Sensors
The multi-sensor module collects data from the motor.
2
ESP32
The ESP32 processes the data and sends it to the Raspberry Pi.
3
Raspberry Pi
The Raspberry Pi receives the data, sorts it, and sends it to
the database.
4
Database
The database stores the data for analysis and visualization.

## Slide 7
Circuit Schematic

## Slide 8
Physical Implementation
Initial design with bread board
Design with perforated board

## Slide 9
Electrical housing
3D design is SolidWorks
3D printed desing

## Slide 10
Final Setup
Electrical housing
ESP32
Network of Sensors
Battery Supply

## Slide 11
Data Communication
The communication protocol for the system is MQTT.
MQTT offers a lightweight, low-bandwidth protocol used in IoT. It works using a publisher-subscriber model and provides greater scalability for IoT applications
The raspberry pi acts as the server that receives data from numerous multi-sensor modules, sorts them and posts to our database

## Slide 12
Data Storage
Data from several devices are stored in an SQL database designed to efficiently handle data for multiple devices with several sensors.

## Slide 13
Data Storage
An API was developed to post data to each table in the database based on the required parameters.
The API required an ID for incoming data so that they can be identified and processed.

## Slide 14
Data Collection Process
1
Vibration Capture
Vibration data was collected at a high sampling rate of 1 kHz to accurately capture the motor's dynamic behavior and avoid aliasing.
2
Speed Monitoring
Speed changes are relatively slow, so the system captured speed data at a lower 100 Hz rate to balance performance and data resolution.
3
Electrical Measurements
Current and voltage were sampled at 2 Hz due to the limitations of the PZEM-004T sensor, providing useful electrical profiles.
4
Thermal Imaging
Thermal images were captured once per minute to monitor temperature changes, a slower variable that does not require high-speed sampling.

## Slide 15
Simple Fault Detection System
Normal healthy motor data collection from accelerometer.
Data transformed from time domain to frequency domain (FFT analysis)
Statistical analysis and Normal distribution data displayed.
FFT results set as the baseline.

## Slide 16
Simple Fault Detection System
New data collected from accelerometer.
FFT performed on new data
Statistical analysis and Normal distribution data displayed.
Mean amplitude and distribution data is compared with baseline using T and KS tests.
System identifies and prints out whether the motor is healthy or faulty.

## Slide 17
SIMULINK MODEL
Induction motor model designed on SIMULINK

## Slide 18
SIMULINK MODEL
Simulink Model
Short circuit fault
Open Circuit fault
Broken Rotor bar

## Slide 19
Open Circuit Fault
Torque and speed of healthy motor
Torque and speed of motor with open circuit fault

## Slide 20
Short Circuit Fault
Torque and speed of healthy motor
Torque and speed of motor with short circuit fault

## Slide 21
Broken Rotor Bar Fault
Torque and speed of motor with broken rotor bar fault
Torque and speed of healthy motor

## Slide 22
Fault Classification
Model Selected: XGBoost Classification Model
This technique builds models sequentially.
It constructs decision trees that corrects the errors of other trees.
It can capture non-linear patterns and can handle missing data which made it suitable for this project.

## Slide 23
Model Implementation
A butterworth filter was used to remove noise from the data
The data was cleaned and FFT was performed to extract dominant frequency domain characteristics.
Feature extraction was performed and the data was combined and labeled based on the faults under consideration.
The model was then trained and cross – validated using the XGBoost Model.

## Slide 24
Machine Learning Classification
Motor States and Accuracy
0 – Normal Operation: 63.49%
1 - Imbalance Fault: 51%
2 – Vertical Misalignment Fault: 99.4%
3 – Horizontal Misalignment Fault: 89.92%
4 – Underhang Fault: 82.99%
5 – Overhang Fault: 38.4%
Overall Accuracy = 71.05%

## Slide 25
ANN Model
The model is a neural network used for multi-class classification
Features used in this model were derived from the FFT of the vibration data.
There are 3 dense layers.
Layer 1: Rectified Linear unit which introduces non-linearity.
Layer 2: Batch Normalization to maintain normalized input
Layer 3: Dropout which prevented overfitting by randomly deactivating neurons

## Slide 26
Machine Learning Classification
Motor States and Accuracy
0 – Normal Operation: 62.92%
1 - Imbalance Fault: 85.93%
2 – Vertical Misalignment Fault: 94.72%
3 – Horizontal Misalignment Fault: 95.17%
4 – Underhang Fault: 42.43%
5 – Overhang Fault: 18.55%
Overall accuracy = 66.63%

## Slide 27
Website
A simple website was developed to explain the system and show results from the data collection and processing

## Slide 28
Motor Data Page
This page displays the data being recorded by the system

## Slide 29
Website Data Analysis Page
This page displays the results of the data analytics to show when a fault has occurred.
It is periodically changed with the new data coming to the system.

## Slide 30
Raspberry Pi Setup
This is a simple setup to exhibit the results of the data processing.
The state of the overall system is showed on the lcd screen.
When faults occur then the screen shows which motor is at fault.

## Slide 31
Conclusion and Future Works
In conclusion, the goal of this project was to develop a system that can monitor the condition of an induction motor and determine when faults occur.
The multi-sensor module designed was able to collect and transmit data that was successfully labeled and process to identify faults using FFTs and Machine Learning
In future works the machine learning model can be further developed to accurately detect all the types of faults.

## Slide 32
Thank You